| Product | Kingspan Kooltherm® K12 Framing Board |
| --- | --- |
| Application | Stud Frame Wall Concrete Wall Brick Veneer Wall Weatherboard Cladding |
| Project |  |
| Architect |  |
| Issue Date |  |

# GENERAL

## Scope of Work – Insulation

Stud Frame Wall

______ mm thick Kingspan Kooltherm® K12 Framing Board installed on the external side of the frame wall to achieve a total thermal resistance of RT______  heat flow in and RT______ heat flow out (TPC Reference No.: ________).

Concrete Wall

______ mm thick Kingspan Kooltherm® K12 Framing Board installed over the furring channel clips to achieve a total thermal resistance of RT______ heat flow in and RT______ heat flow out (TPC Reference No.: ________).

Brick Veneer Wall

______ mm thick Kingspan Kooltherm® K12 Framing Board installed to the external side of the frame wall over the brick ties to achieve a total thermal resistance of RT______ heat flow in and RT______ heat flow out (TPC Reference No.: ________).

Weatherboard Cladding

______ mm thick Kingspan Kooltherm® K12 Framing Board installed on the external side of the frame wall with a minimum 25 mm air gap to the external cladding to achieve a total thermal resistance of RT______  heat flow in and RT______  heat flow out (TPC Reference No.: ________).

## Company Contacts – Insulation

Kingspan Insulation technical contacts

Email: technical@kingspaninsulation.com.au

Telephone: 1300 247 235

Web: www.kingspaninsulation.com.au/Contact-Us/Enquiry

## Manufacturer’s Documents – Insulation

Application & Installation guides, Product brochures, CAD drawings and Certificates & Warranties: www.kingspan.com/au/insulation/downloads.

## Interpretation – Insulation

Definitions

General: For the purposes of this work section the following definitions apply:

- Fire hazard properties: Terminology to NCC A2.4.

- Thermal insulation terminology: To AS/NZS 4859.1.

- Masonry structures terminology: To AS 3700.

## Inspection – Insulation

Notice

Inspection: Give notice to Kingspan Insulation so that inspection may be made of the insulation before it is covered up or concealed.

## Submissions – Insulation

Certification

Certification: CodeMark certificate to be submitted as evidence of compliance with the NCC.

Warranty

Warranty: A Project Specific Warranty provided by Kingspan Insulation must be submitted subsequent to a satisfactory site inspection.

To register your specification for your Project Specific Warranty enter the details here www.kingspaninsulation.com.au/PSW

# MATERIALS

## Product substitution

Other insulation: Conform to Submissions – Insulation, Substitutions in the General requirements work section.

Use of expanded polystyrene (EPS), extruded polystyrene (XPS), rigid foam polyurethane (PU), glasswool, rockwool and / or polyisocyanurate (PIR) insulation other than those specified are not acceptable unless formally accepted by the relevant fire authorities and the  building owners insurance underwriters.

## Marking – Insulation

Identification

General: Deliver materials to the site in the Kingspan original sealed packaging, legibly marked to show the following:

- Manufacturer’s identification.

- Product brand name.

- Product type.

- Quantity.

- Product reference code and batch number.

- Date of manufacture.

## Kingspan Insulation Product – Insulation

Kingspan Kooltherm® K12 Framing Board

Description: Framing insulation board comprising a rigid thermoset phenolic insulation core, faced on both sides with reflective composite aluminium foil, autohesively bonded to the insulation core during manufacture.

- Thickness: _____ mm

- R-value: R_______

- Foil emittance: E0.06

- Board size: 2400 mm x 1200mm

- CodeMark certificate: SAIG-CM20047

www.kingspan.com/au/insulation/downloads

Fire hazard properties

Insulation: When tested to AS 1530.3, Kingspan Kooltherm® K12 Framing Board achieves the following results:

- Ignitability:		9

- Flame spread:		0

- Heat evolved:		1

- Smoke development:	3

The insulation shall have a tested smoke obscuration of not more than 100 m2/kg.

Insulation standard

Insulation: Kingspan Kooltherm® K12 Framing Board complies with AS/NZS 4859.1.

Management standards

Insulation: Kingspan Kooltherm® K12 Framing Board is manufactured under a management system certified to:

- BS/IS EN ISO 9001:2008		Quality Management

- BS/IS EN ISO 14001:2004 	Environmental Management

- BS/IS OHSAS ISO 18001:2007 	Health and Safety Management

## Fasteners and Supports

    - Stud Frame Wall
Large headed galvanised clout nails or screws and external battens placed over the Kingspan Kooltherm® K12.

    - Concrete Wall
Kingspan Kooltherm® K12 will be supported by the furring channel secured by the clips.

    - Brick Veneer Wall
Insulation retaining discs / clips to be approximately 80 mm in diameter.

    - Weatherboard Cladding
Large headed galvanised clout nails or screws.

# EXECUTION

## Fixing to Stud Frame Wall – Insulation

Application

Location: To exterior of the frame.

Fixing

Ensure that stud spacings do not exceed 600 mm centres.

Fix Kingspan Kooltherm® K12 Framing Board to the external surface of the frame structure ensuring vertical board joints coincide with a vertical member.

Ensure that the boards are lightly butted and continuity of insulation is maintained.

Use large headed galvanised clout nails or screws as temporary fixings prior to the secondary support batten being fitted.

Fix preservative treated softwood battens vertically to the wall frame, through the insulation sheathing, ensuring that the battens and fixings are coincident with the underlying timber studs, top and bottom plates.

Consider the weight of cladding when selecting the type of fixing and fixing frequency for the battens.

Fix the external cladding panel to the secondary support batten in the traditional manner.

## Fixing to Concrete Wall – Insulation

Application

Location: Push over furring channel clips.

Fixing

Install chosen furring channel clips at required spacing for plasterboard lining.

Fit Kingspan Kooltherm® over furring channel clips by pushing over the clips to abut the wall, and so that the wings of the clips penetrate the board. Care should be taken to avoid the foil facing of the Kingspan Kooltherm® separating from the insulation core by neatly trimming the foil face at the point where the furring channel clip penetrates the insulation.

Butt join boards of Kingspan Kooltherm® to provide a continuous insulation layer.

Install furring channels by clipping into channel clips. Furring channels should be tight against the face of the Kingspan Kooltherm®. Where furring channels are not tight to the insulation contact Kingspan Insulation Technical Service for further advice.

Install plasterboard lining.

## Fixing to Brick Veneer Wall – Insulation

Application

Location: To exterior of wall frame.

Fixing

Ensure that stud spacings do not exceed 600 mm centres.

Attach appropriate wall ties to frame at spacings required for the masonry external leaf.

Fix Kingspan Kooltherm® K12 Framing Board to the external surface of the frame structure ensuring vertical board joints coincide with a vertical member.

Ensure that the boards are lightly butted and continuity of insulation is maintained.

Use large headed galvanised clout nails or screws as fixings prior to the insulation boards being tied to the frame with an appropriate timber frame wall tie and insulation retaining disc.

Ensure that fixings are coincident with the underlying timber studs, top and bottom wall plates.

Construct the outer leaf of masonry in the conventional manner, using appropriate wall ties to hold the two wall leaves together.

## Fixing for Weatherboard Cladding – Insulation

Application

Location: To exterior of the frame.

Fixing

Ensure that stud spacings do not exceed 600 mm centres.

Fix Kingspan Kooltherm® K12 Framing Board to the external surface of the frame structure ensuring vertical board joints coincide with a vertical member.

Ensure that the boards are lightly butted and continuity of insulation is maintained.

Use large headed galvanised clout nails or screws as temporary fixings prior to the secondary support batten being fitted.

Fix preservative treated softwood battens vertically to the wall frame, through the insulation sheathing, ensuring that the battens and fixings are coincident with the underlying timber studs, top and bottom plates.

Consider the weight of cladding when selecting the type of fixing and fixing frequency for the battens.

Fix the external cladding panel to the secondary support batten in the traditional manner.

Cutting

General: Cutting should be carried out either by using a fine toothed saw, or by scoring with a sharp knife, snapping the board over a straight edge and then cutting the facing on the other side. Ensure accurate trimming to achieve close-butting joints and continuity of insulation.

## Completion – Insulation

Warranties

Warranty: A Project Specific Warranty provided by Kingspan Insulation must be submitted subsequent to a satisfactory site inspection.